## Slide 1
KERALA STATE ENERGY CONSERVATION AWARD – 2023
HLL LIFECARE LIMITED
AKKULAM FACTORY

## Slide 2
OVERVIEW OF HLL AKKULAM FACTORY
Year of inception : 1992
Products : Blood Bags, Surgical Sutures, IUDs
Major Customers : MoH & FW, NACO,UNFPA, IDA,
Domestic trade & international market
Manufacturing Capacity
Blood Bags : 12.50 Million SBE
Surgical Sutures : 6.00 Lakh Dozens
Intra Uterine Device
  Copper T : 5.50 Million Pcs
  Tubal Ring : 2.50 Million Pairs

## Slide 3
CE Mark (blood bags)
as per Latest MDR Regulations- First in India
ISO 14001 :2015
ISO 45001 : 2018
ISO 9001 :2015
INTERNATIONAL QUALITY CERTIFICATIONS
Product Certification
Facility Certifications
ISO 13485 :2016
UNFPA
Anvisa
IDA
Tanzania F& DA

## Slide 4
Biological lab:
  Sterility & Pyrogen tests
  Bio burden tests
GMP/GLP Compliant
QA/QC labs
Physical & Chemical Testing Labs:
  Incoming raw & packing material tests
  In process test
  Final product test

## Slide 5
PRODUCTS
BLOOD BAGS
HL HAEMOPACK BLOOD BAGS
DONATO BLOOD BAGS
Blood Bags manufactured with highest adherence to quality and safety.
Available in a wide range of configurations to meet the modern-day needs of blood transfusion services.

## Slide 6
PRODUCTS
SURGICAL SUTURES
Integral part of any surgical procedure.
Absorbable and non-absorbable surgical sutures for General Surgeries and various other specialties.
HINGLACT, HIDOX, HINCRYL, HINSURG, HISIL,
HILON, HINOCRYL.

## Slide 7
PRODUCTS
INTRA UTERINE DEVICES
Copper T
  T- Care 380A
  M- Care 375
  M- Care 250
Tubal Ring
Emily - Hormone releasing IUS

## Slide 8
Best Safety Performance Award 2023 Awarded by Factories & Boilers GoK, for Medium Scale Industries
AWARDS & RECOGNITIONS
HLL AFT received BEST SAFETY PERFORMANCE award in medium scale industries from Factories and Boilers, Govt. of Kerala, 2022
BEST SAFETY PERFORMANCE AWARD

## Slide 9
AWARDS & RECOGNITIONS
ENERGY CONSERVATION AWARD 2020
In medium scale category from EMC, GoK.
SRESTA SURAKSHA PURASKAR ARD
HLL AFT received the SRESTA SURAKSHA PURASKAR Award for outstanding safety performance in Medium Factories, in connection with the Industrial Safety Award – 2021 awarded by National Safety Council

## Slide 10
MAJOR ENERGY CONSERVATION / GREEN ENERGY INITIATIVES
HLL Akkulam- Overview

## Slide 11: MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY
Biogas Plant- 150 Kg/Day
25 kWp Solar Plant

## Slide 12
Solar Water Heater- 100 Lph
Sky lighting at Storage Area
Avg. Lux level: 250
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 13
Instantaneous Hot Water Generation unit
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 14
VFD for 150 hp Air compressor
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 15
Automatic Level Controller for DM plant
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 16
Energy Efficient Lighting
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 17
Energy efficient Double skin AHUs for clean room
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 18
130 kL capacity Rainwater harvesting system
MAJOR ENERGY CONSERVATION INITIATIVES AT HLL AKKULAM FACTORY

## Slide 19
MAJOR ENERGY CONSERVATION ACTIVITIES, SAVINGS & INVESTMENTS -2022-23

## Slide 20: IMPLEMENTATION OF ADVANCED ENERGY MONITORING SYSTEM
System aids in live monitoring of the energy consumption of all electrical installations including production and utility equipment at HLL Akkulam Factory.
Timely corrective and preventive measures to control and optimize energy consumption.
Product wise actual energy consumption can be obtained instead of estimations .
Total investment | Rs.9.00 LAKH
First year energy cost savings | Rs.8.90 LAKH

## Slide 21: IMPLEMENTATION OF ADVANCED ENERGY MONITORING SYSTEM
HOME PAGE

## Slide 22: IMPLEMENTATION OF ADVANCED ENERGY MONITORING SYSTEM
Advanced energy meters installed at all electrical panels of the factory.
Data from all energy meters are synched with the EMS system in real-time.
Data is being presented in a user-friendly manner in dashboard formats and reports.

## Slide 23: INSTALLATION OF ELECTRICALLY ACTUATED VALVES IN AHUS
Installed Electrically actuated valves to control the chilled water supply in all AHUs in Blood Bag, Cu T and Suture production.
Total investment | Rs 2.5 LAKH
First year energy cost savings | Rs. 1.55 LAKH

## Slide 24: INSTALLATION OF FEEDBACK CONTROL MECHANISM IN AHUs
Installed temperature transmitters in return air duct of AHU’s and based on return air temperature speed of AHU’s varied.
AHU’s speed optimized based on actual load requirement.
Total investment | Rs.1.5 LAKH
First year energy cost savings | Rs. 4.96 LAKH

## Slide 25: INSTALLATION OF VFD IN COOLING TOWER PROCESSING
VFD provided in the cooling tower used for process application. Reduction in energy consumption by 17160 KWH per annum.
Total investment | Rs. 0.75 LAKH
First year energy cost savings | Rs.1.15 LAKH

## Slide 26: MODIFICATION OF CONDENSATE RECOVERY SYSTEM
Condensate recovery system modified by adding Steam traps (TD -13 nos.) in steam consumption areas.
Total investment | Rs. 4.2 LAKH
First year energy cost savings | Rs. 10.74 LAKH

## Slide 27: INSTALLATION OF PRESSURE REDUCING VALVE SYSTEM FOR STEAM PRESSURE OPTIMIZATION
Installed PRV System for steam pressure optimization in NCG tank for Pure Steam Generator, AHU’s for Suture Clean room RH Control and Canteen.
Total investment | Rs. 5.4 LAKH
First year energy cost savings | Rs. 5.2 LAKH

## Slide 28: HOT INSULATION PROVIDED IN UTILITY LINES HOT INSULATION PROVIDED IN UTILITY LINES
Reinsulation of old steam lines carried out (200 m). It resulted in 1.08 % reduction in Furnace oil consumption
Total investment | Rs. 1.55 LAKH
First year energy cost savings | Rs.2.06 LAKH

## Slide 29: HOT INSULATION PROVIDED IN UTILITY LINES INSTALLATION OF INTEGRATED SOLAR STREET LIGHTS
Installation of 10 numbers of 40 W integrated solar street lights with motion sensor. The light will work at 20 W normally and change to 40 W once it senses some motion.
Total investment | Rs. 2.0 LAKH
First year energy cost savings | Rs.0.15 LAKH

## Slide 30
ENERGY CONSERVATION ACTIVITIES SNAP SHOT : 2022-23
Sl No | Description | Investment (Lakh) | Savings in First year (Lakh)
1 | Implementation of Advanced Energy Monitoring System | 9.0 | 8.9
2 | Installation of Pressure Reducing Valve (PRV) System at NCG tank at Pure Steam Generator, Dehumidifier and Canteen. | 5.4 | 5.2
3 | Installation of 3 way valves in Air Handling Units (AHU) | 2.5 | 1.55
4 | Modification of condensate recovery system | 2.08 | 10.74
5 | Hot insulation provided in Utility Lines | 1.55 | 2.06
6 | Installation of feedback control mechanism in AHU | 1.5 | 4.96
7 | Installation of VFD for Fan of 200TR Processing Cooling Tower | 0.75 | 1.15
8 | Installation of 10 nos of integrated solar street lights | 2.0 | 0.15
 | Grand Total | 24.78 | 34.71
Notes: DESCENDING ORDER OF INVESTMENT

## Slide 31
Production | Blood bag (SBE) | Suture (Dozen) | Copper T (MPcs)
2022-23 Q1 to Q3 (Average) | 28,74,207 | 21,625 | 1.91
2022-23 Q4 | 26,96,687 | 25,945 | 2.55
Savings of Rs. 9.58 Lakh by reducing consumption by 12.52%
Savings of Rs. 9.10 Lakh by reducing consumption by 14.51%
Savings of Rs. 0.99 Lakh by reducing consumption by 14.97%.
Chart: 
| 2022-23 (Q1 to Q3)Avg | 2022-23 Q4
 | 106445.02 | 91000.47
FO Consumption (L)
Chart: 
| 2022-23 (Q1 to Q3) Avg | 2022-23 Q4
 | 1134096.6667 | 992140
Electricity Consumption (KWh)
Chart: 
| 2022-23(Q1 to Q3) Avg | 2022-23(Q4)
 | 11977.17 | 10184.5
Water Consumption (kL)
Consumption Analysis 2022-23

## Slide 32
Chart: Electricity Consumption (KWh) (Apr – Dec 23)
| 2022-23 | 2023-24
Electricity Consumption | 3402290 | 2987080
Production | Blood bag (SBE) | Suture (Dozen) | Copper T (MPcs)
2023-24 (Apr to Dec) | 82,81,018 | 80,835 | 4.56
2022-23 (Apr-Dec) | 86,22,621 | 64,877 | 5.72
Savings of Rs. 28.03 Lakh by reducing consumption by 12.20%
Savings of Rs. 39.59 Lakh by reducing consumption by 23.43%
Savings of Rs. 7.06 Lakh by reducing consumption by 34.97%.
Chart: Water Consumption (kL) (Apr – Dec 23)
| 2022-23 | 2023-24
kL | 35931.5 | 23368
Chart: FO Consumption (L) (Apr to Dec 23)
| 2022-23 | 2023-24
FO Consumption (Apr to Oct 2023) | 319335.07 | 244530.15

## Slide 33
TRAININGS & KNOWLEDGE SHARING SESSIONS

## Slide 34
SAFE FORUM ACTIVITIES
Tech fix Forum of Engineering department arranged a knowledge sharing session on the topic “Energy conservation measures”
Tech Fix Safe Forum

## Slide 35
STEAM AND STEAM SYSTEM - TRAINING PROGRAM
Awareness and knowledge sharing program by engaging OEM (M/s Forbes Marshall) to engineering technicians

## Slide 36
THANK YOU